Wi-Fi Media Module is built into LCD Monitors

# Features:

# * Networking Advertisements on Demand.

# * Integrated HDD or CF (optional).

# * High Resolution Output (1080i).

# * Automatic Synchronization With Server Time.

# * Scheduled Download Content From Internet.

# * Scheduled Playback Content at Local or Internet & Scheduled Play, Auto Start Play.

# * Download List Supported.

# * Wi-Fi Supports 802.11 b/g.

# * USB Host 2.0 Storage Class Supported.

# * Network Samba Protocol supported.

* Build WiFi Module in LCD Monitors (10.4”, 12.1”. 15”, 17”, 19”, 20”, 23”, 26”, 32”,

* 37”, 42”, 47”, 55” etc

Hardware Specifications

| Video Output | Composite Video, S-Video, VGA Component Video, SCART |
| --- | --- |
| Video Format, | PAL 576i/576p, NTSC 480i/480p, HDTV 720p/1080i (MPEG 1/2/4, MP3, WMV9, ISO) |
| Audio Output | Stereo, SPDIF Digital Audio Output on Optical. |
| WLAN | Mini PCI Card Slot for IEEE 802.11/b/g |
| Networking | Ethernet 10/100-BaseT, Supports Samba Client, DHCPC, NTP, FTP Client, Http file get. |
| Remote Control | 47 Keys |